Sunshine on My Shoulders

You have been asked by the ACME shirt company to design a shirt that will block the most light for the company's new "Sunblocker" line of shirts. They have given you several fabrics to test. Use a Light Probe to measure how much light is blocked by layers of the different materials.

OBJECTIVES

In this activity, you will

Measure the light intensity as it passes through layers of different kinds of fabrics.

Predict which fabric will block the most light.

Draw conclusions about which fabric would be best for a shirt.

MATERIALS

computer with Logger Lite software installed

Go! Link interface

TI Light Probe

3 strips of different kinds of fabric

several books to hold the Light Probe

meter stick

KEY QUESTION

What makes a material good at keeping light from reaching your skin?

Hypothesis

The 			 fabric will block the most amount of light and the

fabric will block the least amount of light because

PROCEDURE

1.	Do the following to get the Light Probe ready to collect data:

Make sure the Light Probe is connected to the Go! Link and that the Go! Link is connected to the computer.

Get a stack of books that will raise the Light Probe to the level of the light source.

Place the probe so the tip is sticking out about 3 cm in front of the book.

Tape down the probe so it doesn’t move during data collection.

Position the tip of the Light Probe 20 cm from the light source, with the probe pointing directly at the bulb.

2.	Start Logger Lite on your computer.

3.	Open the file for this activity by doing the following:

- Click the Open button, .

Open the file called “Elementary Science.”

Open the file called “34 Sunshine.”

4.	Adjust the position of the Light Probe by doing the following:

- Turn on the lamp.

- Look at the light level reading in the digital meter on the screen. If the reading is higher than 0.95, slide the books away from the lamp until it is below 0.95. Important: Be sure to keep the probe pointing directly at the light bulb.

5.	Now, by doing the following, you will collect data for 3 layers of the same fabric. Careful: Make sure that the book and the Light Probe stay in the same place while you are collecting data!

- Click  to start data collection.

- Click  and enter 0 for the number of layers.

- Place one layer of fabric “A” over the tip of the Light Probe. Be careful not to put your fingers between the probe and the light.

- Click , then enter 1 for the number of layers of fabric, and then click .

- Fold the fabric so that two layers cover the tip of the Light Probe. Click  and enter 2 for the layers of fabric. Click .

- Fold the fabric so that three layers cover the tip of the Light Probe. Click , enter 3 for the layers of fabric, and click .

- Click  to end data collection and then click the Store button, , to save the data from the first fabric

6.	Repeat Step 5 for the other two fabrics.

ANALYZE YOUR DATA

1.	Look at the three runs on the computer screen. Which fabric did the best job of blocking out light?

2.	Did your hypothesis match your results? Use your data to explain your answer.

3.	If you were given three other fabrics, describe the characteristics you might look for to help determine which one would be the best at blocking the light.

4.	Write a formal letter to the ACME shirt company reporting your research and advising them on which material will make a shirt that will block the most light.

Good job!!